## Slide 1
Dimensionality reduction in subsurface modeling
June 13, 2022
Misael M. Morales
Graduate Research Assistant, The University of Texas at Austin
Dr. Michael Pyrcz
Associate Professor, The University of Texas at Austin
Dr. Carlos Torres-Verdin
Professor, The University of Texas at Austin

## Slide 2
2
Executive Summary
Accurate and detailed subsurface models are often too large and/or redundant for practical data science applications.
Dimensionality Reduction is an efficient theme for modeling and simulation of the subsurface, exploiting the hidden features and information in data.
1) We survey different dimensionality reduction techniques, and their usage for subsurface modeling – testing their power for reconstructing subsurface images from reduced dimensional space.
2) We built a forward simulator for CO2 monitoring using a deep learning architecture that exploits the latent space dynamics.
We recommend to work in latent space for subsurface modeling, characterization, and simulation.
Workflows including history matching, closed-loop reservoir management, and robust optimization can be improved by exploiting the latent space.

## Slide 3
Executive Summary
Motivation
PART I: Dimensionality Reduction Techniques
Part II: Hybrid CNN-RNN for CO2 Monitoring
Conclusion
Outline
3

## Slide 4
Motivation
4

## Slide 5
Subsurface spatial data is often very large, and different sources and scales make it difficult to process.
There tends to be a high degree of correlation and structure in 2D/3D subsurface data, which makes it a perfect candidate for latent space analysis and modeling.
Encoder-Decoder architectures allow for efficient latent representation and analysis of subsurface data.
We propose:
A survey of different dimensionality reduction techniques and applications to generic and subsurface data.
A hybrid CNN-RNN proxy model for CO2 monitoring, exploiting latent space dynamics.
5
CNN-RNN for CO2 Monitoring
AutoEncoders for Dimensionality Reduction
Notes: Why we need dimensionality reduction in subsurface modeling
Why encoder-decoder architectures are best
- Project 1: An overview of different dimensionality reduction techniques (classic and modern) and their application to a subsurface dataset
- Project 2: An application of a deep learning-based proxy model that uses latent space dynamics for predicting CO2 migration in the subsurface

## Slide 6
6
Recent Literature
Maldonado-Cruz & Prycz, (2022) J Pet. Sci. Eng.:
  U-Net for surrogate flow model under geologic uncertainty
  Generate saturation maps based on different PV injected from the permeability/porosity realizations
Jo, Pan, Santos, Jung & Pyrcz, (2021) J Pet. Sci. Eng.:
  Machine learning-assisted history matching
  Using GAN for automatic history matching of deepwater lobe systems
Alakeely & Horne, (2020) SPE Res. Eval. Eng.:
  Deep learning models for downhole signal predictions
  Comparison of CNN and RNN for the prediction of downhole rates, pressure, choke setting, etc.
Kim & Durlofsky, (2022) ArXiV:
  CNN-RNN for robust optimization and closed-loop management
  CNN-LSTM architecture from to predict production rates from permeability maps
Kaur, Fomel, et. al., (2022) GeoSci World Interpretation:
  Seismic Inversion via CNN-RNN architecture
  Used a CNN-Transformer architecture to predict permeability from seismic response (forward=perm->sat->seismic)
Notes: Recent advances in Deep Learning applications in petroleum engineering and subsurface modeling (as well as seismic reservoir characterization/inversion)
None have developed image-to-image (or image-to-timelapse images) deep learning proxy! Nor applied it to CO2 monitoring!

## Slide 7
7
PART I
Dimensionality Reduction Techniques
SVD, PCA, Dictionary Learning, FFT & Wavelet, Deep Learning
AutoEncoders for Dimensionality Reduction

## Slide 8
MNIST dataset – 60,000x(28,28)
Subsurface Dimensionality Reduction
Similar architectures from MNIST examples, applied to SPE10 data.
Applications to geologic scenario selection, robust optimization, uncertainty quantification, inverse modeling, …
8
SPE10 data generation process
Notes: All models/techniques are first tested on the MNIST/digits dataset.
Then, we use a preprocessed SPE10 dataset to apply the dimensionality reduction technique to subsurface data!
All is performed using the encoder-decoder architecture that exploits latent space information.

## Slide 9
MNIST Example
Classical dataset for image processing.
Demonstrate the usage of each dimensionality reduction technique with MNIST first.
9
Singular Value Decomposition
Principal Component Analysis
Dictionary Learning
Discrete Fourier Transform
Discrete Wavelet Transform

## Slide 10
SVD
Decompose data matrix, , into 3 components.
Only retain leading terms, removing redundancy and preserving most important features for reconstruction.
170 SV’s retained
MSE=0.003
SSIM=0.970
10
From Wikipedia, SVD
Original (top) and SVD-reconstructed (bottom) realizations
First 36 SVD basis
Notes: SVD is one of the most classical techniques.
It decomposes the data (X) into left-singular-vector (U), singular values (S), and right-singular-vectors (V^T).
170 leading basis for the SVD representation of the SPE10 data, and the reconstruction of the models using the leading SVD’s

## Slide 11
PCA
11
One of the most classical dimensionality reduction techniques.
Eigenvectors of the covariance matrix.
Maximize variance explained in each eigendirection.
Where is the normalized covariance matrix
First 36 PCA basis
80 PC’s retained
MSE=0.010
SSIM=0.873
Original (top) and PCA-reconstructed (bottom) realizations
Notes: PCA is the second most classical technique
PCA basis for the SPE10 model, using only the leading 80 PC’s. And the reconstruction of the models from these leading terms.

## Slide 12
Dictionary Learning
120-atom dictionary
MSE=0.005
SSIM=0.934
12
Exploit sparsity in the representation of data by generating a “dictionary” of “words” that we can combine to reconstruct images.
Uses the K-SVD algorithm to iteratively find the best words/atoms and the best sparse coder to represent the data.
From Kong, et. al. (2020)
Original (top) and Dictionary Learning-reconstructed (bottom) realizations
First 36 Dictionary atoms/words
Notes: If we have a Dictionary of words/atoms that can accurately represent the data, and a Sparse Coder that can point to where we can select the correct words/atoms, then we can reconstruct any model using the combination of words/atoms and codes.
SPE10 leading atoms and reconstruction using a dictionary of only 120 atoms.

## Slide 13
FFT & Wavelet
13
Fast Fourier Transform
40% retained
MSE=0.003 | SSIM=0.965
Original (top) and FFT-reconstructed (bottom) realizations
First 8 FFT representations
Wavelet Transform
30% retained
MSE=0.001 | SSIM=0.989
Original (top) and DWT-reconstructed (bottom) realizations
First 8 DWT representations
Leading techniques for image/video compression.
FFT:
  Generic basis of sines/cosines from eigenvectors.
  Retains frequencies
DWT:
  Multiresolution information
  Spatiotemporal / localized analysis via adaptive filtering bands .
Notes: FFT and DWT are the leading techniques for image/video compression (JPEG, etc.)
FFT uses a generic basis of sines/cosines from the eigenvectors to represent the data. It retains a range of frequencies from the original image. Data is shifted from time-space to frequency-wavenumber domain.
DWT uses generic basis of sines/cosines, but it exploits multiresolution information for spatiotemporal analysis, using adaptive filtering of frequency bands for localized information.
SPE10 FFT/DWT basis for the first few samples. Also, the original and reconstructed images retaining only a percentage of the latent space.

## Slide 14
Deep Learning
Train:
  MSE=0.011
  SSIM=0.867
Test:
  MSE=0.021
  SSIM=0.736
14
CNN-AE training process
CNN-AE architecture
CNN-VAE architecture
MNIST flat
MNIST reconstruct
784
100
50
100
784
FCNN-AE architecture
From compthree.com/blog/autoencoder/
CNN-VAE Train/Test Truth & Predictions
Notes: Deep Learning is very powerful for dimensionality reduction.
A lot of different architectures can be designed (Fully-Connected, Convolutional, Variational, etc.)
3 examples of “vanilla” networks to encode-decode the SPE10 data.
Note: These can be significantly improved with a lot more detailing and fine-tuning, but for this purpose, we just demonstrate the applicability and power of these techniques.

## Slide 15
15
PART II
Hybrid CNN-RNN for CO2 Monitoring
CNN-RNN architecture

## Slide 16
Develop a deep learning framework for forward reservoir simulation of CO2 migration
Exploit latent space dynamics for timelapse predictions using a CNN-RNN architecture
Numerical Simulation
(MRST)
Reservoir Model
(SPE10)
Data Processing
(Python)
Deep Learning
(Keras)
1 injector
CO2
years injection, monitor monthly
Tarbert (Gaussian) + Ness (fluvial)
Reshape to images
Data augmentation (rotation)
Random Shuffling
Min-Max Normalization
Train/Test split
Two-phase water-gas model
FD + Automatic Differentiation
Output: dynamic pressure & saturation fields
&
Encoder: Conv2D
Recurrent: GRU
Decoder: Conv3DTranspose
Compile, Fit & Predict
16
Notes: This project is composed of 4 main parts (reservoir model, numerical simulation, data processing, and the deep learning-based proxy model
The proxy model is CNN-RNN-CNN encoder-decoder structure that exploits latent space dynamics to model a timelapse of saturation from a static permeability input.

## Slide 17
SPE10 model
partition
grid
reservoir
simulation
1. Reservoir Model
17
Timelapse saturation states
Simulator inputs
(60,60)
Permeability
(60,60,60)
Saturation
CNN-RNN
Proxy
ML forward proxy
Full SPE10 model
Partitioned SPE10 model
Notes: Data comes from SPE10
We partition the 220x60x85 model into 255 x (60,60) realizations and use MRST to forward-simulate CO2 injection. We collect 60 saturation states (60 months) for each realization

## Slide 18
High-fidelity simulations are performed using MRST CO2 Lab
255, 2D realizations with 1 injector
  Initially water saturated
  CO2 injection @ 5 m3/day
  5 years, monitored monthly
  Automatic Differentiation framework
Parallelized over 10 cores on an Intel i9-10900K @ 5000 MHz
  seconds per realization
2. Numerical Simulation
18
CO2-Brine relative perm curves
MRST simulator code
HFS input and outputs
Notes: Numerical simulation is done using MRST (in parallel)
CO2Lab module in MRST provides a simplified model for CO2 injection. We use most of the default parameters for CO2 properties
Inject for 5 years, monitored monthly (60 states)
Inject 5 m^3 per day
One injector in the center

## Slide 19
3. Data Processing
HFS sliced into and
Reshape to and
Data augmentation by rotation realizations
Shuffle concatenated dataset
  Make proxy agnostic to orientation, learn true flow physics
Min-Max Normalization
Train (66%), Test (33%) random split
19
Augmented permeability & saturation data
Train/Test distribution for mean input & output
Notes: Data from MRST is then pre-processed in order to have better machine learning
6 preprocessing steps

## Slide 20
4. CNN-RNN Proxy
unfold
20
Encoder-recurrent-decoder architecture to predict dynamic saturation states from permeability
Folded CNN-RNN architecture
Unfolded CNN-RNN architecture
Notes: Schematic of the CNN-RNN model
Left = “Folded” model, where we clearly see the encoder-recurrent-decoder architecture
Right = “Unfolded” model, where we can visualize the latent space dynamics, meaning that the latent vector is expanded into 125 features (5,5,5), and updated according to the saturation map (60,60,60)

## Slide 21
4. CNN-RNN Proxy
Conv2D
Conv2D
BatchNorm
LeakyReLU
MaxPool2D
regularization
LeakyReLU activation
Convolutional block
Conv Block 1
Conv Block 2
Conv Block 3
Conv Block 4
The Encoder
21
CNN-RNN
architecture
Notes: Encoder section
Contains 4 convolutional blocks
Each convolutional block has Conv2D(LeakyRelu)-Conv2D(l2norm)-BatchNorm-LeakyReLu-MaxPool --- the pooling reduces dimensions

## Slide 22
4. CNN-RNN Proxy
The Recurrent block
RepeatVector
Reshape
Flatten
GRU
Flatten
RepeatVector
GRU
Reshape
Recurrent block
22
CNN-RNN
architecture
Notes: Recurrent section
We flatten the latent space, Z (576)
Repeat it 125 times
Apply recurrent layer (GRU, many-to-many) such that (125,576)->(125,128)
Reshape into (5,5,5128) … (length, width, height, channels)

## Slide 23
4. CNN-RNN Proxy
The Decoder
ConvT Block 1
ConvT Block 2
ConvT Block 3
Output Block
ConvT3D
ConvT3D
BatchNorm
LeakyReLU
regularization
LeakyReLU activation
Transpose Convolutional block
ConvT3D
23
CNN-RNN
architecture
Notes: Decoder section
Contains 3 Transpose-Convolutional blocks, and an Output block
Each transpose convolutional block has ConvT3D(LeakyRelu)-ConvT3D(LeakyRelu)-ConvT3D(l2norm)-BatchNorm-LeakyReLu ---- the strides increase dimensions

## Slide 24
4. CNN-RNN Proxy
Compile
  Optimizer = Nadam (Adam with Nesterov Momentum)
Fit
  Epochs = 300
  Batch Size = 40
  Validation split = 0.25
17 minutes on Nvidia RTX 3080
24
CNN-RNN
architecture
CNN-RNN Training process
Notes: We then compile and fit the model
We use Nadam, Nesterov Adam. A slight update in the momentum calculation. Works better than Adam for this problem (very small learning rate)
Use a Loss function that combines MSE (pixel-wise) and SSIM (overall image)
SSIM ~ luminance, contrast, perceptual information
Overfit! 

## Slide 25
4. CNN-RNN Proxy
Training: MSE=0.016 | SSIM=0.817
25
CNN-RNN
architecture
Training samples
Training inputs
Training predictions
Notes: Training predictions
Very good!

## Slide 26
4. CNN-RNN Proxy
Testing: MSE=0.040 | SSIM=0.563
26
CNN-RNN
architecture
Testing samples
Testing inputs
Testing predictions
Notes: Testing Predictions
Not so good, but still useful. Can be improved!

## Slide 27
HFS 20 seconds per realization
RNN-CNN architecture: 930,000 parameters
  0.5 milliseconds per realization 40,000 speedup
Applications:
  Uncertainty quantification
  Inverse modeling
  History matching / model calibration
  Closed-loop / Robust optimization
Other areas:
  Groundwater flows
  Contaminant transport
  Hydrocarbon production
Results
27
CNN-RNN for latent-space history matching
CNN-RNN for inverse modeling
Notes: Significant speedup in the forward simulation
Architecture can be used for other applications

## Slide 28
Conclusion
28

## Slide 29
Subsurface data must be treated in reduced-dimensional space for efficiency, at little or no loss of detail.
Classical techniques vs. Deep Learning
  Accuracy, cost/efficiency, application-specific
Plethora of applications in reservoir modeling, characterization, and simulation.
Future Studies include:
  Development of the CNN-RNN Proxy for CO2 Monitoring
  Integration of other data sources (seismic, fiber optic) for improved proxy model predictions
  Robust optimization and closed-loop reservoir management using CNN-RNN Proxy
Conclusion
29
Notes: Dimensionality reduction is crucial for subsurface modeling.
In modern times, where we have all this data, our computers would allow us to make gigantic models and use all the data in the world, but that is just not realistically possible.
Dimensionality reduction techniques allow for usage of large data, without using all of it, just the important/leading features, and still have very good predictions and results, at higher efficiency.
Dimensionality reduction via deep learning can be applied to almost any area of subsurface energy engineering.

## Slide 30
Thank you
Q&A
Misael Morales
PhD Student in Petroleum & Geosystems Engineering
Advisors: Dr. Michael Pyrcz, Dr. Carlos Torres-Verdin
GitHub | Linkedin | Website | misaelmorales@utexas.edu

## Slide 31
Backup Slides

## Slide 32
References
Maldonado-Cruz, Eduardo, and Michael J Pyrcz. (2022) “Fast Evaluation of Pressure and Saturation Predictions with a Deep Learning Surrogate Flow Model.” Journal of petroleum science & engineering 212
Kim, Y. D., & Durlofsky, L. J. (2022). "Convolutional-Recurrent Neural Network Proxy for Robust Optimization and Closed-Loop Reservoir Management." arXiv preprint arXiv:2203.07524.
Kaur, Harpreet et al. (2022) “Time-Lapse Seismic Data Inversion for Estimating Reservoir Parameters Using Deep Learning.” Interpretation (Tulsa) 10.1
S. Pan, S.L. Brunton, and J.N. Kutz (2022) "Neural Implicit Flow: a mesh-agnostic dimensionality reduction paradigm of spatio-temporal data." arXiv preprint arXiv:2204.03216
Joon, Shams, Dawuda, Ismael, Morgan, Eugene, and Sanjay Srinivasan. (2022) "Rock Physics-Based Data Assimilation of Integrated Continuous Active-Source Seismic and Pressure Monitoring Data during Geological Carbon Storage." SPE Journal.
Gonzalez, Keyla, and Siddharth Misra. (2022) “Unsupervised Learning Monitors the Carbon-Dioxide Plume in the Subsurface Carbon Storage Reservoir.” Expert systems with applications 201
K.G. Gurjao, E. Gildin, R. Gibson, and M. Everett. (2022) "Estimation of Far-Field Fiber Optics Distributed Acoustic Sensing DAS Response Using Spatio-Temporal Machine Learning Schemes and Improvement of Hydraulic Fracture Geometric Characterization." SPE Hydraulic Fracturing Technology Conference and Exhibition, USA
Salazar, Jose J et al. (2022) “Fair Train-Test Split in Machine Learning: Mitigating Spatial Autocorrelation for Improved Prediction Accuracy.” Journal of petroleum science & engineering 209:109885–.
Tang, Meng, Yimin Liu, and Louis J Durlofsky. (2021) “Deep-Learning-Based Surrogate Flow Modeling and Geological Parameterization for Data Assimilation in 3D Subsurface Flow.” Computer methods in applied mechanics and engineering 376:113636–.
H. Jo, Y. Cho, M.J. Pyrcz, H. Tang, and P. Fu (2021) "Machine learning-based porosity estimation from spectral decomposed siesmic data." arXiv preprint arXiv:2111.13581
Wen, Gege, Catherine Hay, and Sally M Benson. (2021) “CCSNet: A Deep Learning Modeling Suite for CO2 Storage.” Advances in water resources 155:104009–.
Alsulaimani, Thamer , and Mary Wheeler. (2021) "Reduced-Order Modeling for Multiphase Flow Using a Physics-Based Deep Learning." SPE Reservoir Simulation Conference
E.J.R. Coutinho, M.J. Aqua and E. Gildin. (2021) "Physics-Aware Deep-Learning-Based Proxy Reservoir Simulation Model Equipped with State and Well Output Prediction." SPE Reservoir Simulation Conference, Virtual.
Ciriello, V., Lee, J. & Tartakovsky, D.M. (2021) "Advances in uncertainty quantification for water resources applications." Stoch Environ Res Risk Assess 35, 955–957
Pan, W., Torres-Verdín, C. & Pyrcz, M.J. (2021) "Stochastic Pix2pix: A New Machine Learning Method for Geophysical and Well Conditioning of Rule-Based Channel Reservoir Models." Nat Resour Res 30, 1319–1345
Wu, Hao et al. (2021) “A Multi-Dimensional Parametric Study of Variability in Multi-Phase Flow Dynamics During Geologic CO2 Sequestration Accelerated with Machine Learning.” Applied energy 287:116580–.
Santos, J.E., Yin, Y., Jo, H. et al. (2021) "Computationally Efficient Multiscale Neural Networks Applied to Fluid Flow in Complex 3D Porous Media." Transp Porous Med 140, 241–272
Chan, S., Elsheikh, A.H. (2020) "Data-driven acceleration of multiscale methods for uncertainty quantification: application in transient multiphase flow in porous media." Int J Geomath 11,3
Cheung, S.W., Chung, E.T., Efendiev, Y. et al. (2020) "Deep global model reduction learning in porous media flow simulation." Comput Geosci 24, 261–274
Almasov, Azad , Onur, Mustafa , and Albert C. Reynolds. (2020) "Production Optimization of the CO2 Huff-N-Puff Process in an Unconventional Reservoir Using a Machine Learning Based Proxy." SPE Improved Oil Recovery Conference, Virtual
Jiang, Chiyu lmaxr et al. (2020) “MESHFREEFLOWNET: A Physics-Constrained Deep Continuous Space-Time Super-Resolution Framework.” SC20: International Conference for High Performance Computing, Networking, Storage and Analysis. IEEE 1–15.
J. Nagoor Kani, Elsheikh, A.H. (2019) "Reduced-Order Modeling of Subsurface Multi-phase Flow Models Using Deep Residual Recurrent Neural Networks." Transp Porous Med 126, 713–741
Jayne, Richard S, Hao Wu, and Ryan M Pollyea. (2019) “Geologic CO2 Sequestration and Permeability Uncertainty in a Highly Heterogeneous Reservoir.” International journal of greenhouse gas control 83.C:128–139.
K.-A. Lie. (2019) "An Introduction to Reservoir Simulation Using MATLAB/GNU Octave: User Guide for the MATLAB Reservoir Simulation Toolbox (MRST)." Cambridge University Press
Brunton, Steven L., and Jose Nathan Kutz. (2019) "Data-Driven Science and Engineering: Machine Learning, Dynamical Systems, and Control." 1st ed. Cambridge University Press
Guo, Zhenyu, and Albert C Reynolds. (2018) “Robust Life-Cycle Production Optimization With a Support-Vector-Regression Proxy.” SPE journal 23.6:2409–2427
Naraghi, Morteza Elahi, Spikes, Kyle , and Sanjay Srinivasan. (2017) "3D Reconstruction of Porous Media From a 2D Section and Comparisons of Transport and Elastic Properties." SPE Res Eval & Eng 20:342–352
Ampomah, W et al. (2017) “Optimum Design of CO2 Storage and Oil Recovery Under Geological Uncertainty.” Applied energy 195
J. Nagoor Kani, Elsheikh, A.H. (2017) "DR-RNN: A deep residual recurrent neural network for model reduction." arXiv preprint arXiv:1709.00939
32

## Slide 33
Simulation Variables
Reference pressure: mega Pascals
Reference temperature:
Water compressibility:
Rock compressibility: bars
Water viscosity: Pascal-second
CO2 viscosity: Pascal-second
Residual water saturation:
Residual CO2 saturation:
Water viscosity: 1000
Grid size: 60x60x1
Grid dimensions: 20x10x5 ft
Initial reservoir pressure: psia
Initial reservoir saturation: -
Total simulation time: 5 years
Monitor steps: 1 month
Total steps: 60
Wellbore radius: 0.05
AD Solver: TwoPhaseWaterGasModel
33

## Slide 34
Proxy Model Variables
L2 regularization: 1e-4
LeakyReLU alpha: 0.3
RNN dropout: 0.2
Nadam learning rate: 5e-4
34